## Slide 1: 3D Compton Imaging: A new modality for Nuclear Medecine at 511 KeV and above
Damavan Imaging
10/2020
Authors A. Iltis1, G. Zeufack1, M. Lopez1, H. Snoussi2, L. Zimmer3,4, N. Costes3, C. Bouillot3, Z. Hmissi1, F. Lavenne3, J. Redoute3
1Damavan Imaging, Rosieres pres Troyes, FRANCE,
2Université de Technologie de Troyes (UTT), Troyes, FRANCE,
3CERMEP-Imagerie du vivant, Bron, FRANCE,
4INSERM, CNRS, Université de Lyon, Lyon, FRANCE

## Slide 2: Temporal δ Compton camera: How does it work?
Image from time
10/2020

## Slide 3: How does it work?
The principle of Compton Camera:
A Probabilistic map of cone intersections
3
Compton events detected on 2 successive plates
A cone which includes the incident photon direction is calculated
The source is found by intersecting many cones
Retro- projection image is then done
Notes: One cone per photon => many cones needed => a number of events (statistics) necessary

## Slide 4: How does it work?
2D Vs 3D Compton imaging
4
Single view = 2D All the cones share the same origin
Ambiguity of reconstruction on the axis of view
3 Views (X,Y,Z) = 3DSampling of all space direction
No Ambiguity of reconstruction
More precise position
Notes: One cone per photon => many cones needed => a number of events (statistics) necessary

## Slide 5: How does it work?
Compton 2D and 3D imaging tools
5

## Slide 6: What does Compton imaging bring to medical imaging?
Image from time
10/2020

## Slide 7
What does Compton imaging bring to medical imaging?
7
Ease of use and Wide Field of View:
90°x90° in one image
The set-up
FOV of our camera 50cm
Visible and Gamma

## Slide 8
Capacity to make good images at high energy (1,3 MeV) with low dose (Radiotherapy)
X-Ray
Imaging 60Co
1.3 MeV at 1.3 m
4.5 MBq / 20 min
What does Compton imaging bring to medical imaging?
8
Notes: A gamma-mage gated on the energy 1332 KeV (here we see only the activity of 60Co) shows that the main source in the bottom right corner corresponds to 60Co. The image is much clearer, because most diffused photons are excluded.
One can also see the contour of the small barrel, likely scattered photons on the solid body of the small barrel or Co powder accumulation on it.
No 60Co on the upper third of the drum is visible => different source (RONA: what is it in this case = glass wool).

## Slide 9
Images of weak sources till natural background
glass plate from its natural 228Ac contamination
What does Compton imaging bring to medical imaging?
9

## Slide 10
What does Compton imaging bring to medical imaging?
10
Comparison of 3D Compton with existing nuclear medicine modalities
 | SPECT | PET | Compton 3D
Energy range | 50-250 KeV | 511 KeV | 400-2000 KeV
Detector acceptance angle | 5° x 5° | 0,2° x 0,2° | 90° x 90°
Spatial resolution | +/- 0,2 cm3 | 0,03 cm3 | <0,3 cm3 TBD
Reconstruction method | 2D retroprojection | sinogram | 3D Cone intersection
Notes: A gamma-mage gated on the energy 1332 KeV (here we see only the activity of 60Co) shows that the main source in the bottom right corner corresponds to 60Co. The image is much clearer, because most diffused photons are excluded.
One can also see the contour of the small barrel, likely scattered photons on the solid body of the small barrel or Co powder accumulation on it.
No 60Co on the upper third of the drum is visible => different source (RONA: what is it in this case = glass wool).

## Slide 11: Temporal δ Compton camera 3D imaging
Image from time
10/2020
Notes:       CeBr3 = Cerium Bromide
      Z effective: between 1 atom of Ce and 3 atoms of Brome
      Spatial resolution in the crystal: 1.5 mm
    Extremely short time vetoes => Invalid events can be discarded in our temporal system if:
  The relationship θn = f (E1/ Eg ) is incorrect (partial energy deposition)
  The events P1 and P2 are not within tight time limits (<300 ps).
      very effective photons detection: + 50% more photons captured for the same time
      faster acquisition: 30-50%
      Depth Of Interaction (DOI)

## Slide 12
Temporal δ Compton camera 3D imaging
12
Images 2D vs 3D: 22Na sources (15 KBq)
2D reconstruction
Source apparent size 3cm
3D reconstruction : 2D slice
No artefacts
Source size = 2 cm = actual size

## Slide 13
Temporal δ Compton camera 3D imaging
13
3D slices of a 80mm mouse (5000 photons)
Glucose18F / 0.51 MBq /3 x 10mn Views
22Na vs 137Cs : 20cm seen from 50cm
22Na vs 137Cs : 20 cm seen from 50 cm

## Slide 14
Temporal δ Compton camera 3D imaging
14
Future steps: dedicated 3D scanner

## Slide 15: 3D Compton Imaging: A new modality for Nuclear Medecine at 511 keV and above
Damavan Imaging
10/2020
Alain.iltis@damavan-imaging.com
www.damavan-imaging.com